### Polyhedral MEA Fabrication Protocol
#### Materials and Tools Needed
1. 320 Micrometer Diameter Wires: 64 wires, differential, or as many wires as your DAQ supports.
2. Clear Plastic Sheet: Thick enough to hold its shape.
3. Drill: Precision micro-drill bits (about 480 micrometer diameter).
4. Pourable Clear Silicone.
5. Epoxy or Silicone Sealant: For encapsulating and securing wires.
6. FreeEEG32 or Other Data Acquisition Board.
#### Step-by-Step Implementation
##### Step 1: Design and Prepare the Plastic Sheet
1. Cut the Plastic Sheet into Polyhedron Shape Panels:
  1. 1 square (top square is not included since it needs an opening to pour the silicone): 2cm x 2cm.
  2. 4 rectangles: 2cm x 4cm.
  3. 8 trapezoids: top side 4cm, bottom side 2cm, other sides 2cm.
2. Design the Grid:
  1. Design a grid with an almost equal number of holes per sheet (depends on the amount of signals your DAQ supports, divided by 13 sides, plus the amount of stimulation electrodes you can use). The top side is used for wires to come out of, this gives you a total of 32 holes for the FreeEEG32 or as many as your DAQ supports, plus the number of holes for each stimulation electrode you have.
3. Drill the Holes:
  1. Use micro-drill bits to drill 480 micrometer diameter holes in the plastic sheet.
  2. Ensure the holes are clean and precisely spaced.
##### Step 2: Insert the Wires
1. Prepare the Wires:
  1. Cut the 320 micrometer diameter wires to the desired length, ensuring they are long enough to extend out of the polyhedron for cutting the tips off later.
2. Insert the Wires into the Holes:
  1. Carefully insert the wires into the drilled holes in each plastic panel.
  2. Ensure the wires are evenly inserted and extend out of the sides of the panel for cutting the tips off later.
3. Glue the Panels Together to Form the Polyhedron:
  1. This leaves the top of the polyhedron open for pouring in the silicone.
##### Step 3: Embed the Wires in Silicone
1. Prepare the Silicone:
  1. Mix the silicone according to the manufacturer's instructions.
2. Pour the Silicone:
  1. Pour the silicone into the polyhedron.
  2. Allow the silicone to flow around the wires and into the holes, encapsulating the wires. Make sure to get rid of any bubbles by tapping or mixing.
3. Cure the Silicone:
  1. Allow the silicone to cure completely as per the manufacturer’s instructions.
  2. Ensure the wires remain in place during the pouring and curing process.
##### Step 4: Extract the Molded Electrode Array
1. Remove the Plastic Polyhedron Molding Case:
  1. Once the silicone is fully cured, carefully remove the plastic casing.
  2. The wires should be securely embedded in the silicone, with the ends extending out.
2. Trim the Wires:
  1. Trim the wires to the desired length, ensuring they are uniform and suitable for connections.
3. Surface Preparation:
  1. Use fine-grit sandpaper (e.g., 400-600 grit) to gently roughen the surface of the silicone. This creates micro-abrasions that increase the surface area for bacterial adhesion.
    1. Procedure: Lightly sand the silicone surface in a circular motion until it has a uniformly rough texture. Clean the surface with isopropyl alcohol or sterile water to remove any debris.
  2. Poly-L-lysine soak/spray for 1 hour.
##### Step 5: Connect the Wires to FreeEEG32 / DAQ
1. Connect the Wires:
  1. Connect the wires to the FreeEEG32 or your data acquisition board as per the board’s instructions and configuration.

#### Shape and example layout of electrodes